## LANCOM България ООД

## София 1330, ул. Гюешево №83,

## Бизнес Център Сердика, сграда 2, офис 108

## тел.: +359 2 920 0561, 920 0563

факс: +359 2 920 0584 www.lancombg.om

# Text boxes

AS/AD/A2 Server/Networking Cabinets   	   Стр. 02-17

WM Single Section Wall mounted Cabinets 	   Стр. 18-20

ZH Double Section Wall-mounted Cabinets       Стр. 21-23

OR Open Racks                            		   Стр. 24-25

Power Distribution Unit                      	   	   Стр. 26

Аксесоари                                		   Стр. 27-00

Create Classic Project

Show Elegant Quality

КАТАЛОГ

AS/AD/A2 Networking Cabinets

A2 front door

AS front door

AD front door

Double-section  high-density vented door

Double-section high-density Vented plate door

Rear door with hexagonal holes

High-density vented rear door

AS/AD/A2 Networking Cabinets

Width 600mm AS/AD/A2 Networking Cabinets

Meaning of second order No.(front door)

| AS.■■■■.■■■ | AD.■■■■.■■■ | A2.■■■■.■■■ |
| --- | --- | --- |
| AS front door （tempered glass door & vented door border） | AD front door （hexagonal reticular high-density vented door） | A2 front door (toughened glass door & plate door border) |

Meaning of last second order No. (rear door)

| ■■.■■■■.■0■ | ■■.■■■■.■1■ | ■■.■■■■.■2■ | ■■.■■■■.■3■ | ■■.■■■■.■4■ |
| --- | --- | --- | --- | --- |
| Plate rear door without holes | Rear door with hexagonal holes | High-density vented rear door | Double-section rear door | Double-section high-density vented door |

Optional accessories

| Specification | Packs of | Unit | Material | Surface finish |
| --- | --- | --- | --- | --- |
| Fan unit with Thermostat | 1 | Set | Body SPCC | Powder coated |
| Thermostat | 1 | Set | Body SPCC | Powder coated |
| PDU（Germany） | 1 | Pc | --- | --- |
| PDU（UL） | 1 | Pc | --- | --- |
| PDU | 1 | Pc | --- | --- |
| Plinth | 1 | Set | T1.2/T3.0 SPCC | Powder coated |
| Filter for fan unit | 2 | Set | ABS | --- |
| Fixed shelf | 1 | Pc | T1.2 SPCC | Powder coated |
| Square screw & nut | 10 | Set | Steel | Color Zinc |

Structure of width 600mm AS/AD/A2 cabinet structure

Optional plinth to meet under-base wiring, ventilation & rat-proof

1U/2U metal cable management with cap

Earthing kit

Keyboard tray with mouse panel

Main parts with earthing kit hole can connect with each other

Lockable cable entry

Adjustable mounting profile

& mounting angle

Removable front door

Shunting rail

U mark mounting rail

1. Top cover     2. Fan unit       3. Mounting profile      4. Mounting angle        5. Door with hexagonal holes      6. High-density vented door

7. Steel door without hole     8. Bottom panel     9. 2” heavy duty castor    10. Frame    11. Side panel     12. A2 front door   14 .AS front door

Width 800mm AS/AD/A2 Networking Cabinets

Metal cable management

slot with cap

Fan unit

Width 800mm A2 cabinet with metal cable management slot

1. Top cover         2. Fan unit         3. Mounting profile        4. Spacer          5. Mounting angle        6. Rear door with hexagonal holes     7. High-density vented rear door         8. Steel rear door without hole          9. Bottom panel       10. 2” heavy duty castor         11. Frame  12. Side panel        13. Cable management slot       14. A2 front door       15.AD front door      16. AS front door

Structure of width 800mm AS/AD/A2

| Model No. | W*D | Capacity |
| --- | --- | --- |
| SEAS.6842.710 | 600*800 | 42U |

| Model No. | W*D | Capacity |
| --- | --- | --- |
| SEAS.6842.911 | 600*800 | 42U |

Material:

- SPCC cold rolled steel;

Thickness: mounting profile 2.0mm, mounting angle 1.5mm, others 1.2mm;

Surface finish:

- Degreasing, pickling, phosphoric, powder coated

Standard:

- Comply with ANSI/EIA RS-310-D, IEC297-2, DIN41494; PART1, DIN41494; PART7, ETSI standard;

Loading capacity:

- Static loading: 800KG

Degree of Protection:

- IP20

Feature:

- Exquisite design with precise dimension and craftsmanship;

- Toughened glass door with silk-screened flower pattern, vented front door border and rear door;

- Adjustable feet and heavy duty castors are available simultaneously;

- Cable entry on the top cover and bottom panel with adjustable sizes;

- Optional installation of plinth to enable cabinets fixation, under-base cable entry/ventilation;

- Efficient and reliable cabinet connection by baying kit;

- Removable side panels to ease maintain;

- Around 1/3 assembled original volume when flat pack.

AS Server Cabinets

Ornament strip

Color

| RAL9004 | RAL7035 |
| --- | --- |

Definition of body color

| ■■.■■■■.■■0 | ■■.■■■■.■■1 |
| --- | --- |
| gray | black |
| RAL7035 | RAL9004 |

Definition of ornament strip color

| AS.■■■■. 7■■ | AS.■■■■. 9■■ |
| --- | --- |
| Light Red | Light blue |

Specification

| Model No. | Capacity ( U ) | Width (mm) | Depth (mm) | Height (mm) | Packing Dimension W*D*H | Volume (CBM) |
| --- | --- | --- | --- | --- | --- | --- |
| SEAS.6618. ■■■ | 18 | 600 | 600 | 988 | 670*670*1028 | 0.4615 |
| SEAS.6818. ■■■ |  |  | 800 |  | 670*870*1028 | 0.5992 |
| SEAS.6018. ■■■ |  |  | 1000 |  | 670*1070*1028 | 0.7370 |
| SEAS.6622. ■■■ | 22 | 600 | 600 | 1166 | 670*670*1196 | 0.5369 |
| SEAS.6822. ■■■ |  |  | 800 |  | 670*870*1196 | 0.6971 |
| SEAS.6022. ■■■ |  |  | 1000 |  | 670*1070*1196 | 0.8574 |
| SEAS.6627. ■■■ | 27 | 600 | 600 | 1388 | 670*670*1418 | 0.6460 |
| SEAS.6827. ■■■ |  |  | 800 |  | 670*870*1418 | 0.8266 |
| SEAS.6027. ■■■ |  |  | 1000 |  | 670*1070*1418 | 1.0166 |
| SEAS.6632. ■■■ | 32 | 600 | 600 | 1610 | 670*670*1640 | 0.7362 |
| SEAS.6832. ■■■ |  |  | 800 |  | 670*870*1640 | 0.9560 |
| SEAS.6032. ■■■ |  |  | 1000 |  | 670*1070*1640 | 1.1757 |
| SEAS.6637. ■■■ | 37 | 600 | 600 | 1833 | 670*670*1863 | 0.8363 |
| SEAS.6837. ■■■ |  |  | 800 |  | 670*870*1863 | 1.0859 |
| SEAS.6037. ■■■ |  |  | 1000 |  | 670*1070*1863 | 1.3356 |
| SEAS.6237. ■■■ |  |  | 1200 |  | 670*1270*1863 | 1.5852 |
| SEAS.6642. ■■■ | 42 | 600 | 600 | 2055 | 670*670*2085 | 0.9360 |
| SEAS.6842. ■■■ |  |  | 800 |  | 670*870*2085 | 1.2153 |
| SEAS.6042. ■■■ |  |  | 1000 |  | 670*1070*2085 | 1.4947 |
| SEAS.6242. ■■■ |  |  | 1200 |  | 670*1270*2085 | 1.7741 |
| SEAS.8642. ■■■ |  | 800 | 600 |  | 870*670*2085 | 1.2513 |
| SEAS.8842. ■■■ |  |  | 800 |  | 870*870*2085 | 1.5781 |
| SEAS.8042. ■■■ |  |  | 1000 |  | 870*1070*2085 | 1.9409 |
| SEAS.8242. ■■■ |  |  | 1200 |  | 870*1270*2085 | 2.3037 |
| SEAS.6647. ■■■ | 47 | 600 | 600 | 2277 | 670*670*2307 | 1.0356 |
| SEAS.6847. ■■■ |  |  | 800 |  | 670*870*2307 | 1.3448 |
| SEAS.6047. ■■■ |  |  | 1000 |  | 670*1070*2307 | 1.6539 |
| SEAS.6247. ■■■ |  |  | 1200 |  | 670*1270*2307 | 1.9630 |

Main Dimension

Main parts

| S/N | Specification | Quantity | Unit | Material | Surface Finish | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Top cover | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 2 | Mounting profile | 4 | Piece | SPCC cold rolled steel t2.0 | Blue zinc | --- |
| 3 | Mounting angle | 6 | Piece | SPCC cold rolled steel t1.5 | Powder coated | 4pcs for lower 32U |
| 4 | Cable management slot | 2 | Piece | SPCC cold rolled steel t0.8 | Powder coated | --- |
| 5 | Spring lock | 1 | Piece | --- | Black | With 2 keys |
| 6 | Toughened glass front door doordoor | 1 | Piece | Toughened glass/ t1.2 SPCC | Powder coated | Round vented border |
| 7 | 2’’ heavy duty castor | 4 | Piece | --- | --- | --- |
| 8 | Frame | 2 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 9 | Side panel | 2 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 10 | Small round lock | 1 | Piece | --- | Nickel coated | With 2 keys |
| 11 | Hexagonal-hole rear door | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | Hexagonal vent |
| 12 | Bottom panel | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 13 | Spacer | 12 | Piece | SPCC cold rolled steel t2.0 | Powder coated | 8pcs for lower 32U |
| 14 | M6 B-head screw | 20 | Piece | Steel | Color Zinc | 40pcs for over 32U |
| 15 | M6 square nut | 20 | Piece | Steel | Color Zinc | 40pcs for over 32U |
| 16 | Allen wrench | 1 | Piece | Steel | Black | --- |
| 17 | M12 adjustable Feet | 4 | Piece | --- | --- | --- |

Width 800mm AS Server Cabinets

Main Dimension

Main parts

| S/N | Specification | Quantity | Unit | Material | Surface finish | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Top cover | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 2 | Mounting profile | 4 | Piece | SPCC cold rolled steel t2.0 | Blue zinc | --- |
| 3 | Mounting angle | 6 | Piece | SPCC cold rolled steel t1.5 | Powder coated | 4pcs for lower 32U |
| 4 | Spring lock | 1 | Piece | --- | Black | With 2 keys |
| 5 | Toughened glass front door | 1 | Piece | Toughened glass/ t1.2 SPCC | Powder coated | Round vented border |
| 6 | 2’’ heavy duty castor | 4 | Piece | --- | --- | --- |
| 7 | Frame | 2 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 8 | Side panel | 2 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 9 | Small round Lock | 1 | Piece | --- | Nickel coated | With 2 keys |
| 10 | Hexagonal-hole rear door | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | Hexagonal vent |
| 11 | Bottom panel | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 12 | M6 B-head screw | 20 | Piece | Steel | Color zinc | 40 pcs for over 32U |
| 13 | M6 square nut | 20 | Piece | Steel | Color zinc | 40 pcs for over 32U |
| 14 | Allen wrench | 1 | Piece | Steel | Black | --- |
| 15 | M12 adjustable feet | 4 | Piece | --- | --- | --- |

Width 600mm AS Server Cabinets

AS Server Cabinets

AD Server Cabinets

Material:

- SPCC cold rolled steel;

Thickness: mounting profile 2.0mm, mounting angle 1.5mm, others 1.2mm

；                  ；

| Model No. | W*D | Capacity |
| --- | --- | --- |
| SEAD.6642.920 | 600*600 | 42U |

Spring Lock

Earthing holes for main parts

High-density vented door enable protection, ventilation and reliable operation, the ventilated rate is 71%

Surface finish:

- Degreasing, pickling, phosphoric, powder coated

Standard:

- Comply with ANSI/EIA RS-310-D, IEC297-2, DIN41494; PART1, DIN41494;PART7 ETSI standard;

Loading capacity:

- Static loading: 800KG

Degree of protection:

- IP20

Feature:

- Hexagonal reticular high-density vented front door (patent) & rear door for protection, ventilation and reliable operation.

- Exquisite image (patent) with precise dimension and craftsmanship.

- Lockable cable entry on top cover and bottom panel with adjustable sizes.

- Optional plinth enables cabinets to stay in a fixed position while meeting requirements of under-base wiring/ventilation and rat prevention.

- Strong cabinet connection by baying kit (patent).

- Spring lock.

Width 600mm AD Server Cabinets

## Main parts

| S/N | Specification | Quantity | Unit | Material | Surface finish | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Top cover | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 2 | Mounting profile | 4 | Piece | SPCC cold rolled steel t2.0 | Blue zinc | --- |
| 3 | Mounting angle | 6 | Piece | SPCC cold rolled steel t1.5 | Powder coated | 4pcs for lower 32U |
| 4 | Spring lock | 2 | Piece | --- | Black | With 4 keys |
| 5 | Hexagonal reticular high-density vented front door | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 6 | 2” heavy duty castor | 4 | Piece | --- | --- | --- |
| 7 | Frame | 2 | Set | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 8 | Side panel | 2 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 9 | High-density vented rear door | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 10 | Bottom panel | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 11 | M6 B-head screw | 20 | Piece | Steel | Color Zinc | 40pcs for over 32U |
| 12 | M6 square nut | 20 | Piece | Steel | Color Zinc | 40pcs for over 32U |
| 13 | Allen wrench | 1 | Piece | Steel | Black | --- |
| 14 | M12 adjustable feet | 4 | Piece | --- | --- | --- |

### Main dimension

Width 800mm AD Server Cabinets

### Main parts

| S/N | Specification | Quantity | Unit | Material | Surface finish | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Top cover | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 2 | Mounting profile | 4 | Piece | SPCC cold rolled steel t2.0 | Blue zinc | --- |
| 3 | Mounting angle | 6 | Piece | SPCC cold rolled steel t1.5 | Powder coated | 4pcs for lower 32U |
| 4 | Cable management slot | 2 | Piece | SPCC cold rolled steel t0.8 | Powder coated | --- |
| 5 | Spring lock | 2 | Piece | --- | Black | With 4 keys |
| 6 | Hexagonal reticular high-density vented front door | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 7 | 2” heavy duty castor | 4 | Piece | --- | --- | --- 300KGS |
| 8 | Frame | 2 | Set | Steel t1.2 | Powder coated | --- |
| 9 | Side door | 2 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 10 | High-density vented rear door | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 11 | Bottom | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 12 | Connecting block | 12 | Piece | SPCC cold rolled steel t2.0 | Powder coated | 8pcs for lower 32U |
| 13 | M6 B-head screw | 20 | Piece | Steel | Color Zinc | 40pcs for over32U |
| 14 | M6 square nut | 20 | Piece | Steel | Color Zinc | 40pcs for over32U |
| 15 | Inner 6-angle wrench | 1 | Piece | Steel | Black | --- |
| 16 | M12 feet | 4 | Piece | --- | --- | --- |

## Main dimension

AD Server Cabinets

Specification

| Model No. | Capacity ( U ) | Width (mm) | Depth (mm) | Height (mm) | Packing Dimension W*D*H | Volume (CBM) |
| --- | --- | --- | --- | --- | --- | --- |
| SEAD.6618. ■■■ | 18 | 600 | 600 | 988 | 670*670*1028 | 0.4615 |
| SEAD.6818. ■■■ |  |  | 800 |  | 670*870*1028 | 0.5992 |
| SEAD.6018. ■■■ |  |  | 1000 |  | 670*1070*1028 | 0.7370 |
| SEAD.6622. ■■■ | 22 | 600 | 600 | 1166 | 670*670*1196 | 0.5369 |
| SEAD.6822. ■■■ |  |  | 800 |  | 670*870*1196 | 0.6971 |
| SEAD.6022. ■■■ |  |  | 1000 |  | 670*1070*1196 | 0.8574 |
| SEAD.6627. ■■■ | 27 | 600 | 600 | 1388 | 670*670*1418 | 0.6460 |
| SEAD.6827. ■■■ |  |  | 800 |  | 670*870*1418 | 0.8266 |
| SEAD.6027. ■■■ |  |  | 1000 |  | 670*1070*1418 | 1.0166 |
| SEAD.6632. ■■■ | 32 | 600 | 600 | 1610 | 670*670*1640 | 0.7362 |
| SEAD.6832. ■■■ |  |  | 800 |  | 670*870*1640 | 0.9560 |
| SEAD.6032. ■■■ |  |  | 1000 |  | 670*1070*1640 | 1.1757 |
| SEAD.6637. ■■■ | 37 | 600 | 600 | 1833 | 670*670*1863 | 0.8363 |
| SEAD.6837. ■■■ |  |  | 800 |  | 670*870*1863 | 1.0859 |
| SEAD.6037. ■■■ |  |  | 1000 |  | 670*1070*1863 | 1.3356 |
| SEAD.6237. ■■■ |  |  | 1200 |  | 670*1270*1863 | 1.5852 |
| SEAD.6642. ■■■ | 42 | 600 | 600 | 2055 | 670*670*2085 | 0.9360 |
| SEAD.6842. ■■■ |  |  | 800 |  | 670*870*2085 | 1.2153 |
| SEAD.6042. ■■■ |  |  | 1000 |  | 670*1070*2085 | 1.4947 |
| SEAD.6242. ■■■ |  |  | 1200 |  | 670*1270*2085 | 1.7741 |
| SEAD.8642. ■■■ |  | 800 | 600 |  | 870*670*2085 | 1.2513 |
| SEAD.8842. ■■■ |  |  | 800 |  | 870*870*2085 | 1.5781 |
| SEAD.8042. ■■■ |  |  | 1000 |  | 870*1070*2085 | 1.9409 |
| SEAD.8242. ■■■ |  |  | 1200 |  | 870*1270*2085 | 2.3037 |
| SEAD.6647. ■■■ | 47 | 600 | 600 | 2277 | 670*670*2307 | 1.0356 |
| SEAD.6847. ■■■ |  |  | 800 |  | 670*870*2307 | 1.3448 |
| SEAD.6047. ■■■ |  |  | 1000 |  | 670*1070*2307 | 1.6539 |
| SEAD.6247. ■■■ |  |  | 1200 |  | 670*1270*2307 | 1.9630 |
| SEAD.8647. ■■■ |  | 800 | 600 |  | 870*670*2307 | 1.3448 |
| SEAD.8847. ■■■ |  |  | 800 |  | 870*870*2307 | 1.7462 |
| SEAD.8047. ■■■ |  |  | 1000 |  | 870*1070*2307 | 2.0673 |
| SEAD.8247. ■■■ |  |  | 1200 |  | 870*1270*2307 | 2.5490 |

Color

| RAL9004 | RAL7035 |
| --- | --- |

Definition of body color

| ■■.■■■■.■■0 | ■■.■■■■.■■1 |
| --- | --- |
| gray | black |
| RAL7035 | RAL9004 |

Material:

- SPCC cold rolled steel;

Thickness: mounting profile 2.0mm, mounting angle 1.5mm, others 1.2mm

| Model No. | W*D | Capacity |
| --- | --- | --- |
| SEA2.6642.700 | 600*600 | 42U |

Surface Finish:

- Degreasing, pickling, phosphoric, powder coated

Standard:

- Comply with ANSI/EIA RS-310-D, IEC297-2, DIN41494;PART1, DIN41494; PART7, ETSI standard;

Loading Capacity:

- Static loading: 500KG

Degree of Protection:

- IP20

Feature:

- Exquisite design with precise dimension and craftsmanship;

- Toughened glass front door with silk-screened flower pattern, door border and steel rear door;

- Adjustable feet and heavy duty castors are available at the same time;

- Several lockable cable entry on top cover and bottom panel with adjustable sizes;

- Optional plinth enables cabinet to stay in a fixed position, meeting requirements of under-base cable entry/ventilation and prevention;

- Efficient cabinet baying kit(patent);

- Removable side panels, easy to install and maintain;

- Around 1/2~2/3 of original assembled volume when flat pack.

Plate door border

Adjustable mounting profile and profile and mounting angle

Lockable cable entry

Fan Unit

A2 Networking Cabinets

## Main dimension

Main parts

| S/N | Specification | Quantity | Unit | Material | Surface Finish | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Top cover | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 2 | Mounting profile | 4 | Piece | SPCC cold rolled steel t2.0 | Blue zinc | --- |
| 3 | Mounting angle | 6 | Piece | SPCC cold rolled steel t1.5 | Powder coated | 4pcs for lower 32U |
| 4 | Small round lock | 2 | Piece | --- | Nickel coated | With 4 keys |
| 5 | Toughened glass front door | 1 | Piece | Toughened glass/ SPCCt1.2 | Powder coated | --- |
| 6 | 2” heavy duty castor | 4 | Piece | --- | --- | --- |
| 7 | Frame | 2 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 8 | Side panel | 2 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 9 | Steel rear door | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 10 | Bottom panel | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 11 | M6 B-head screw | 20 | Piece | Steel | Color Zinc | 40pcs for over 32U |
| 12 | M6 square nut | 20 | Piece | Steel | Color Zinc | 40pcs for over 32U |
| 13 | Allen wrench | 1 | Piece | Steel | Black | --- |
| 14 | M12 adjustable feet | 4 | Piece | --- | --- | --- |

Width 600mm A2 Networking Cabinets

## Main dimension

Main parts

| S/N | Specification | Quantity | Unit | Material | Surface Finish | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Top cover | 1 | Piece | SPCC Cold rolled steel t1.2 | Powder coated | --- |
| 2 | Mounting profile | 4 | Piece | SPCC Cold rolled steel t2.0 | Blue zinc | --- |
| 3 | Mounting angle | 6 | Piece | SPCC Cold rolled steel t1.5 | Powder coated | 4pcs for lower 32U |
| 4 | Cable management slot | 2 | Piece | SPCC Cold rolled steel t0.8 | Powder coated | --- |
| 5 | Small round lock | 2 | Piece | --- | Nickel coated | With 4 keys |
| 6 | Toughened glass front door | 1 | Piece | Toughened glass/ SPCC t1.2 | Powder coated | --- |
| 7 | 2” heavy duty castor | 4 | Piece | --- | --- | --- |
| 8 | Frame | 2 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 9 | Side panel | 2 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 10 | Steel rear door | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 11 | Bottom panel | 1 | Piece | SPCC cold rolled steel t1.2 | Powder coated | --- |
| 12 | Spacer | 12 | Piece Piece | SPCC cold rolled steel t2.0 | Powder coated | 8pcs for lower 32U |
| 13 | M6 B-head screw | 20 | Piece | Steel | Color Zinc | 40pcs for over 32U |
| 14 | M6 square nut | 20 | Piece | Steel | Color Zinc | 40pcs for over 32U |
| 15 | Allen wrench | 1 | Piece | Steel | Black | --- |
| 16 | M12 Adjustable feet | 4 | Piece | --- | --- | --- |

Width 800mm A2 Networking Cabinets

Color

| RAL9004 | RAL7035 |
| --- | --- |

Definition of ornament strip color

| A2.■■■■. 7■■ | A2.■■■■. 9■■ |
| --- | --- |
| Light Red | Light blue |

Definition of body color

| ■■.■■■■.■■0 | ■■.■■■■.■■1 |
| --- | --- |
| gray | black |
| RAL7035 | RAL9004 |

Specification

| Model No. | Capacity ( U ) | Width (mm) | Depth (mm) | Height (mm) | Packing Dimension W*D*H | Volume (CBM) |
| --- | --- | --- | --- | --- | --- | --- |
| SEA2.6618. ■■■ | 18 | 600 | 600 | 988 | 670*670*1028 | 0.4615 |
| SEA2.6818. ■■■ |  |  | 800 |  | 670*870*1028 | 0.5992 |
| SEA2.6018. ■■■ |  |  | 1000 |  | 670*1070*1028 | 0.7370 |
| SEA2.6622. ■■■ | 22 | 600 | 600 | 1166 | 670*670*1196 | 0.5369 |
| SEA2.6822. ■■■ |  |  | 800 |  | 670*870*1196 | 0.6971 |
| SEA2.6022. ■■■ |  |  | 1000 |  | 670*1070*1196 | 0.8574 |
| SEA2.6627. ■■■ | 27 | 600 | 600 | 1388 | 670*670*1418 | 0.6460 |
| SEA2.6827. ■■■ |  |  | 800 |  | 670*870*1418 | 0.8266 |
| SEA2.6027. ■■■ |  |  | 1000 |  | 670*1070*1418 | 1.0166 |
| SEA2.6632. ■■■ | 32 | 600 | 600 | 1610 | 670*670*1640 | 0.7362 |
| SEA2.6832. ■■■ |  |  | 800 |  | 670*870*1640 | 0.9560 |
| SEA2.6032. ■■■ |  |  | 1000 |  | 670*1070*1640 | 1.1757 |
| SEA2.6637. ■■■ | 37 | 600 | 600 | 1833 | 670*670*1863 | 0.8363 |
| SEA2.6837. ■■■ |  |  | 800 |  | 670*870*1863 | 1.0859 |
| SEA2.6037. ■■■ |  |  | 1000 |  | 670*1070*1863 | 1.3356 |
| SEA2.6237. ■■■ |  |  | 1200 |  | 670*1270*1863 | 1.5852 |
| SEA2.6642. ■■■ | 42 | 600 | 600 | 2055 | 670*670*2085 | 0.9360 |
| SEA2.6842. ■■■ |  |  | 800 |  | 670*870*2085 | 1.2153 |
| SEA2.6042. ■■■ |  |  | 1000 |  | 670*1070*2085 | 1.4947 |
| SEA2.6242. ■■■ |  |  | 1200 |  | 670*1270*2085 | 1.7741 |
| SEA2.8642. ■■■ |  | 800 | 600 |  | 870*670*2085 | 1.2513 |
| SEA2.8842. ■■■ |  |  | 800 |  | 870*870*2085 | 1.5781 |
| SEA2.8042. ■■■ |  |  | 1000 |  | 870*1070*2085 | 1.9409 |
| SEA2.8242. ■■■ |  |  | 1200 |  | 870*1270*2085 | 2.3037 |
| SEA2.6647. ■■■ | 47 | 600 | 600 | 2277 | 670*670*2307 | 1.0356 |
| SEA2.6847. ■■■ |  |  | 800 |  | 670*870*2307 | 1.3448 |
| SEA2.6047. ■■■ |  |  | 1000 |  | 670*1070*2307 | 1.6539 |
| SEA2.6247. ■■■ |  |  | 1200 |  | 670*1270*2307 | 1.9630 |
| SEA2.8647. ■■■ |  | 800 | 600 |  | 870*670*2307 | 1.3448 |
| SEA2.8847. ■■■ |  |  | 800 |  | 870*870*2307 | 1.7462 |
| SEA2.8047. ■■■ |  |  | 1000 |  | 870*1070*2307 | 2.0673 |
| SEA2.8247. ■■■ |  |  | 1200 |  | 870*1270*2307 | 2.5490 |

A2 Networking Cabinets

Removable side panels (side locks optional)

Lockable fan holes and cable entry

Mounting panel

Easy installation, dust -proof

Inside fixation by nuts to avoid accident

Install to wall

| Model No. | W*D | Capacity |
| --- | --- | --- |
| SEWM6409.901 | 600*450 | 9U |

Material:

- SPCC Cold Rolled Steel;

- Thickness：Mounting profile: 1.5mm, others: 1.2mm

Surface Finish:

- Degreasing, pickling, phosphoric, powder coated

Standard:

- Comply with ANSI/EIA RS-310-D, DIN41497 part 1, IEC297-2,

DIN41494 part 7, GB/T3047.2-92 standard

Loading Capacity:

- 60KG

Degree of Protection:

- IP20

Feature:

- Welded frame, reliable structure;

- Standing or wall mounting installation;

- Adjustable feet and heavy duty castors are optional;

- Easy mounting installation（patent）;

- 19” standard installation;

- Removable side panels, side locks optional

- Cable entry on both of top cover and bottom panel;

- 120mm fan available;

- Turning angle of front door is over 180 degrees;

WM Single Section Wall mounted Cabinets

## Main dimension

1.  Frame

2.  Side panel

3.  Mounting panel

4.  Cable entry cover

5.  Fan cover

6.  Mounting profile

7.  Front door

8.  Lock

Main structure

WM Single Section Wall mounted Cabinets

Main parts

| S/N | Specification | Quantity | Unit | Material | Surface finish | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Frame | 1 | Piece | SPCC Cold rolled steel t1.2 | Powder coated | --- |
| 2 | Side panel | 2 | Piece | SPCC Cold rolled steel t1.2 | Powder coated | --- |
| 3 | Mounting panel | 1 | Piece | SPCC Cold rolled steel t1.2 | Powder coated | --- |
| 4 | Cable entrance cover | 2 | Piece | SPCC Cold rolled steel t1.2 | Powder coated | --- |
| 5 | Fan cover | 2 | Piece | SPCC Cold rolled steel t1.2 | Powder coated | --- |
| 6 | Mounting profile | 4 | Piece | SPCC Cold rolled steel t1.5 | Powder coated | --- |
| 7 | Front door① | 1 | Piece | 5MM toughed glass door/ SPCCt1.2 | Powder coated | --- |
| 8 | Lock② | 1 | Piece | --- | --- | With 2 keys |
| 9 | M6 Square nut | 10 | Piece | Steel | Color zinc | 20pcs for over 12U |
| 10 | M6 B-head screw | 10 | Piece | Steel | Color zinc | 20pcs for over 12U |
| 11 | Allen wrench | 1 | Piece | Steel | Black | --- |

Remark：①Three types of front door: toughened glass door, toughened glass door with vented door border, plate front door.

②Toughened glass door and plate front door with small round lock, toughened glass door with vented door border with spring lock.

Definition of ornament strip color

(for toughened glass door with vented door border)

| WM.■■■■.71■ | WM.■■■■.91■ |
| --- | --- |
| Light red | Light blue |

Color

| RAL9004 | RAL7035 |
| --- | --- |
| black | gray |

Definition of front door

| Model No. | Feature |
| --- | --- |
| WM.■■■■.■0■ | Toughened glass door |
| WM.■■■■.■1■ | Toughened glass door with vented border |
| WM.■■■■.■2■ | Plate front door |

Definition

| Model No. | Color |
| --- | --- |
| WM.■■■■.■■1 | RAL9004 |
| WM.■■■■.■■2 | RAL7035 |

Specification

| Model No. | Capacity (U) | Width (mm) | Depth (mm) | Height (mm) | Packing dimension W*D*H | Volume (CBM) |
| --- | --- | --- | --- | --- | --- | --- |
| SEWM.6406.9■■ | 6 | 600 | 450 | 368 | 670*520*430 | 0.1498 |
| SEWM.6606.9■■ |  |  | 600 |  | 670*670*430 | 0.1930 |
| SEWM.6409.9■■ | 9 | 600 | 450 | 501 | 670*520*560 | 0.1951 |
| SEWM.6609.9■■ |  |  | 600 |  | 670*670*560 | 0.2513 |
| SEWM.6412.9■■ | 12 | 600 | 450 | 635 | 670*520*695 | 0.2421 |
| SEWM.6612.9■■ |  |  | 600 |  | 670*670*695 | 0.3106 |
| SEWM.6415.9■■ | 15 | 600 | 450 | 769 | 670*520*830 | 0.2888 |
| SEWM.6615.9■■ |  |  | 600 |  | 670*670*830 | 0.3725 |
| SEWM.6418.9■■ | 18 | 600 | 450 | 901 | 670*520*960 | 0.3344 |
| SEWM.6618.9■■ |  |  | 600 |  | 670*670*960 | 0.4309 |
| SEWM.6422.9■■ | 22 | 600 | 450 | 1082 | 670*520*1140 | 0.3971 |
| SEWM.6622.9■■ |  |  | 600 |  | 670*670*1140 | 0.5117 |
| SEWM.6427.9■■ | 27 | 600 | 450 | 1304 | 670*520*1365 | 0.4755 |
| SEWM.6627.9■■ |  |  | 600 |  | 670*670*1365 | 0.6127 |

Remark: Above packing dimension and volume is for packing with PU foam on four angles; If no PU foam, the packing dimension should decrease

50mm, 50mm, 40mm accordingly, so does the volume.

WM Single Section Wall mounted Cabinets

Adjustable mounting profiles

Side door lock (optional)

No side door lock (standard)

| Model No. | W*D | Capacity |
| --- | --- | --- |
| SEZH.6409.901 | 600*550 | 9U |

Material:

- SPCC cold rolled steel;

- Thickness: Mounting profile 1.5mm,others 1.2mm

；                  ；

Surface Finish:

- Degreasing, pickling, phosphoric, powder coated

Standard:

- Comply with ANSI/EIA RS-310-D, DIN41497 part 1, IEC297-2,

DIN41494 part 7 GB/T3047.2-92 standard

Loading capacity:

- 60KG

Degree of protection:

- IP20

Feature:

- Double section welded frame structure;

- Easy operation and maintaining at the back;

- 19” standard installation;

- Removable side panels, side locks are optional, easy installing and maintaining;

- Cable entry at the top cover and bottom panel;

- 120mm fan optional;

- Turning angle of front door is above 180 degrees;

- Turning angle of rear door is above 90 degrees.

ZH Double Section Wall Mounted Cabinets

Main dimension

Main structure

1. Cable entry cover

2. Back ppanel

3. Frame

4. Side panel

5. Mounting profile

6. Lock

7. Front door

8. Fan cover

ZH Double Section Wall Mounted Cabinets

Main parts

| S/N | Specification | Quantity | Unit | Material | Surface Finish | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Cable entry cover | 3 | Piece | SPCC Cold rolled steel t1.2 | Powder coated | --- |
| 2 | Back panel | 1 | Piece | SPCC Cold rolled steel t1.2 | Powder coated | --- |
| 3 | Frame | 1 | Piece | SPCC Cold rolled steel t1.2 | Powder coated | --- |
| 4 | Side panel | 2 | Piece | SPCC Cold rolled steel t1.2 | Powder coated | --- |
| 5 | Mounting profile | 4 | Piece | SPCC Cold rolled steel t1.5 | Powder coated | --- |
| 6 | Lock① | 2 | Piece | --- | --- | With 4 keys |
| 7 | Front door② | 1 | Piece | Toughened glass door/ t1.2 SPCC | Powder coated | --- |
| 8 | Fan cover | 2 | Piece | SPCC Cold rolled steel t1.2 | Powder coated | --- |
| 9 | M6 square nut | 10 | Piece | Steel | Color zinc | 20pcs for over 12U |
| 10 | M6 B-head screw | 10 | Piece | Steel | Color zinc | 20pcs for over 12U |
| 11 | Allen wrench | 1 | Piece | Steel | Black | --- |

Definition of Ornament strip color

(for toughened glass door with vented door border)

| ZH.■■■■.71■ | ZH.■■■■.91■ |
| --- | --- |
| Light red | Light blue |

Color

| RAL9004 | RAL7035 |
| --- | --- |
| black | gray |

Definition of front door

| Model No. | Feature |
| --- | --- |
| ZH.■■■■.■0■ | Toughened glass door |
| ZH.■■■■.■1■ | Toughened glass door with vented border |
| ZH.■■■■.■2■ | Plate front door |

Definition of Color

| Model No. | Color |
| --- | --- |
| ZH.■■■■.■■1 | RAL9004 |
| ZH.■■■■.■■2 | RAL 7035 |

Remark: Toughened glass door and plate front door with small round lock, toughened glass door with vented door border with spring lock.

Three types of front door: toughened glass door, toughened glass door with vented door border, plate front door.

Specification

| Model No. | Capacity (U) | Width (mm) | Depth (mm) | Height (mm) | Packing Dimension W*D*H | Volume (CBM) |
| --- | --- | --- | --- | --- | --- | --- |
| SEZH.6406.9■■ | 6 | 600 | 550 | 368 | 670*620*430 | 0.1786 |
| SEZH.6409.9■■ | 9 |  |  | 501 | 670*620*560 | 0.2326 |
| SEZH.6412.9■■ | 12 |  |  | 635 | 670*620*695 | 0.2887 |
| SEZH.6415.9■■ | 15 |  |  | 769 | 670*620*830 | 0.3447 |
| SEZH.6418.9■■ | 18 |  |  | 901 | 670*620*960 | 0.3987 |
| SEZH.6422.9■■ | 22 |  |  | 1082 | 670*620*1140 | 0.4736 |
| SEZH.6427.9■■ | 27 |  |  | 1304 | 670*620*1365 | 0.5670 |
| SEZH.6606.9■■ | 6 | 600 | 600 | 368 | 670*670*430 | 0.1930 |
| SEZH.6609.9■■ | 9 |  |  | 501 | 670*670*560 | 0.2513 |
| SEZH.6612.9■■ | 12 |  |  | 635 | 670*670*695 | 0.3106 |
| SEZH.6615.9■■ | 15 |  |  | 769 | 670*670*830 | 0.3725 |
| SEZH.6618.9■■ | 18 |  |  | 901 | 670*670*960 | 0.4309 |
| SEZH.6622.9■■ | 22 |  |  | 1082 | 670*670*1140 | 0.5117 |
| SEZH.6627.9■■ | 27 |  |  | 1304 | 670*670*1365 | 0.6127 |

Remark: Above packing dimension and volume is for packing with PU foam on four angles; if no PU foam, the packing dimension should decrease

50mm, 50mm, 40mm accordingly, so does the volume.

ZH Double Section Wall Mounted Cabinets

OR Open Racks

| Model No. | W*D | Capacity |
| --- | --- | --- |
| SEOR.6642.902 | 600*600 | 42U |

Material:

- SPCC cold rolled steel;

- Thickness: plinth: 2.0mm;

Front and bottom beams：2.0mm, Pole: 1.5mm.

Surface finish:

- Degreasing, pickling, phosphoric, powder coated

Standard:

- Comply with ANSI/EIA RS-310-D, IEC297-2、DIN41491, PART1, DIN41494, PART7 GB/T3047.2-92 standard.

Loading Capacity:

- Static loading: 150KG

Feature:

- Modular design, easily assemble and disassemble for delivery, low-cost.

- Various optional accessories according to requirements (cable management slot, removable working panel, etc.,).

OR Open Racks

Main Dimension

## Main Structure

1. Pole   2. Plinth   3. Horizontal beam   4. Heavy duty castor

Color

| RAL9004 | RAL7035 |
| --- | --- |
| black | gray |

Definition of color

| Model No. | Color |
| --- | --- |
| OR.■■■■.■■1 | RAL9004 |
| OR.■■■■.■■2 | RAL7035 |

Main parts

| S/N. | Specification | Quantity | Unit | Material | Surface finish | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Pole | 2 | Piece | SPCC Cold rolled steel t1.5 | Powder coated | --- |
| 2 | Plinth | 2 | Piece | SPCC Cold rolled steel t2.0 | Powder coated | --- |
| 3 | Horizontal beam | 2 | Piece | SPCC Cold rolled steel t2.0 | Powder coated | --- |
| 4 | 2” heavy duty castor | 4 | Piece | --- | --- | --- |
| 5 | Square screw & nut | 10 | Set | Steel | Color Zinc | --- |
| 6 | Allen wrench | 1 | Piece | Steel | Black | --- |

Specification

| Model No. | Capacity (U) | Width (mm) | Depth (mm) | Height (mm) | Dimension W*D*H | Volume (CBM) |
| --- | --- | --- | --- | --- | --- | --- |
| OR.6622.90■ | 22 | 600 | 600 | 1119 | 670*150*1149 | 0.1155 |
| OR.6632.90■ | 32 | 600 | 600 | 1562 | 670*150*1592 | 0.1600 |
| OR.6637.90■ | 37 | 600 | 600 | 1785 | 670*150*1815 | 0.1824 |
| OR.6642.90■ | 42 | 600 | 600 | 2007 | 670*150*2037 | 0.2047 |
| OR.6647.90■ | 47 | 600 | 600 | 2230 | 670*150*2260 | 0.2271 |

Power Distribution Unit

Power distribution unit

- Supplied as equipment power

- 19” installation

- Multiple specification optional

Parameter:

- 1.8m-length cable

- With or without main switch for power input

Power distribution unit

- Supplied as equipment power

- Design in module

- Multiple socket outlet for all electronical consumptions

Parameter:

- 3m-length cable

- A main switch for power input

Parameter of PDU

| Specification | Reference | V/HZ | A | Standard |
| --- | --- | --- | --- | --- |
| German-type |  | 250V/50-60Hz | 16A | DIN49440（Germany） |

Definition of Color

| Model No. | Color |
| --- | --- |
| PD.■■■■.■■1 | RAL9004 |
| PD.■■■■.■■2 | RAL7035 |

Color

| RAL9004 | RAL7035 |
| --- | --- |
| black | gray |

Specification

| Model No. | Specification | Remark |
| --- | --- | --- |
| SEPD.0504.00■ | 5-outlet German-type PDU | German-type with main switch,1.8m-length,19” installation, with 19”install panel(in color black/white) |
| SEPD.0604.000 | 6-outlet German-type PDU | with main switch,3.0m-length cable,19” installation(only black) |
| SEPD.0804.000 | 8-outlet German-type PDU | with main switch,3.0m-length cable, without mounting material(only black) |
| SEPD.1004.000 | 10-outlet German-type PDU | with main switch,3.0m-length cable, without mounting material(only black) |
| SEPD.1204.000 | 12-outlet German-type PDU | with main switch,3.0m-length cable, without mounting material(only black) |
| SEPD.1504.000 | 15-outlet German-type PDU | with main switch,3.0m-length cable, without mounting material(only black) |

Specification

| Model No. | Specification | Dimension(MM) | Use |
| --- | --- | --- | --- |
|  |  | W | D1 | D2 |  |
| SESA.6002.00■ | 60 Fixed shelf | 470 | 350 | 260 | 19” installation for 600-depth cabinets |
| SESA.8002.00■ | 80 Fixed shelf | 470 | 550 | 460 | 19” installation for 800-depth cabinets |
| SESA.9002.00■ | 90 Fixed shelf | 470 | 650 | 560 | 19” installation for 900-depth cabinets |
| SESA.9102.00■ | 100 Fixed shelf | 470 | 710 | 620 | 19” installation for 1000-depth cabinets |
| SESA.8602.00■ | 60 Extra-fixed shelf | 670 | 350 | 260 | 27” installation for 600-depth cabinets, remove cable management slot and spacer |
| SESA.8802.00■ | 80 Extra-fixed shelf | 670 | 550 | 460 | 27” installation for 800-depth cabinets, remove cable management slot and spacer |
| SESA.8902.00■ | 90 Extra-fixed shelf | 670 | 650 | 560 | 27” installation for 900-depth cabinets, remove cable management slot and spacer |
| SESA.8102.00■ | 100 Extra-fixed shelf | 670 | 710 | 520 | 27” installation for 1000-depth cabinets, remove cable management slot and spacer |

Loading capacity:

- 60 KG

Color:

- RAL9004

- RAL7035

#### Fixed shelf

Used for placing equipment

Material:

- t1.2 SPCC cold rolled steel

Surface Finish:

- Degreasing, pickling,

рhosphoric, powder coat

Fixed shelf

## Dimension

Аксесоари

Definition of color: SA.■■■■. ■■1:RAL9004        SA.■■■■. ■■2:RAL7035

Loading Capacity:

- 100 KG

Color:

- RAL9004

- RAL7035

### Dimension

Specification                                                                Definition of color:  SA.■■■■. ■■1:RAL9004           SA.■■■■. ■■2:RAL7035

| Model No. | Specification | Dimension(MM) | Use |
| --- | --- | --- | --- |
|  |  | W | D1 | D2 |  |
| SESA.6003.00■ | 60 Heavy duty fixed shelf | 470 | 350 | 260 | 19” installation for 600-depth cabinets |
| SESA.8003.00■ | 80 Heavy duty fixed shelf | 470 | 550 | 460 | 19” installation for 800-depth cabinets |
| SESA.9003.00■ | 90 Heavy duty fixed shelf | 470 | 650 | 560 | 19” installation for 900-depth cabinets |
| SESA.9103.00■ | 100 Heavy duty fixed shelf | 470 | 710 | 620 | 19” installation for 1000-depth cabinets |
| SESA.8603.00■ | 60 Extra-Heavy duty fixed shelf | 670 | 350 | 260 | 27” installation for 600-depth cabinets, remove cable management slot and spacer |
| SESA.8803.00■ | 80 Extra-Heavy duty fixed shelf | 670 | 550 | 460 | 27” installation for 800-depth cabinets, remove cable management slot and spacer |
| SESA.8903.00■ | 90 Extra-Heavy duty fixed shelf | 670 | 650 | 560 | 27” installation for 900-depth cabinets, remove cable management slot and spacer |
| SESA.8103.00■ | 100 Extra-Heavy duty fixed shelf | 670 | 710 | 520 | 27” installation for 1000-depth cabinets, remove cable management slot and spacer |

Heavy-duty fixed shelf

For applications when heavy loads up to 100kg

Material:

- SPCC Cold rolled steel t1.2

Surface Finish:

- Degreasing, pickling,

Phosphoric, powder coat

Heavy-duty fixed shelf

## Dimension

Adjustable Feet

Specification

| Model No. | SpecificationΦ | Loading Capacity (KG) |
| --- | --- | --- |
| SESA.0025.010 | M10 adjustable Feet | 280 |
| SESA.0025.012 | M12 adjustable Feet | 320 |

#### Adjustable Feet

Support and make cabinet stable

Material:

- Steel

Surface Finish:

- Carbonic black

Specification

| Model No. | Specification | Dimension(MM) | Use |
| --- | --- | --- | --- |
|  |  | D |  |
| SESA.6002.10■ | 60 Fixed shelf with mounting ear | 350 | 19” installation for 600-depth cabinets |
| SESA.8002.10■ | 80 Fixed shelf with mounting ear | 550 | 19” installation for 800-depth cabinets |
| SESA.9002.10■ | 90 Fixed shelf with mounting ear | 650 | 19” installation for 900-depth cabinets |
| SESA.9102.10■ | 100 Fixed shelf with mounting ear | 710 | 19” installation for 1000-depth cabinets |

Loading capacity:

- 60 KG

Color:

- RAL9004

- RAL7035

Fixed shelf with mounting ear

## Dimension

#### Fixed shelf with mounting ear

Used for placing equipment

Material:

- t1.2 SPCC cold rolled steel

Surface Finish:

- Degreasing, pickling,

phosphoric, powder coat

Аксесоари

Definition of color: SA.■■■■. ■■1:RAL9004       SA.■■■■. ■■2:RAL7035

Loading Capacity:

- 100 KG

Color:

- RAL9004

- RAL7035

### Dimension

Specification                                                                 Definition of color: SA.■■■■. ■■1:RAL9004        SA.■■■■. ■■2:RAL7035

| Model No. | Specification | Dimension(MM) | Use |
| --- | --- | --- | --- |
|  |  | D |  |
| SESA.6003.10■ | 60 Heavy duty fixed shelf with mounting ear | 350 | 19” installation for 600-depth cabinets |
| SESA.8003.10■ | 80 Heavy duty fixed shelf with mounting ear | 550 | 19” installation for 800-depth cabinets |
| SESA.9003.10■ | 90 Heavy duty fixed shelf with mounting ear | 650 | 19” installation for 900-depth cabinets |
| SESA.9103.10■ | 96 Heavy duty fixed shelf with mounting ear | 710 | 19” installation for 960/1000-depth cabinets |

Heavy-duty fixed shelf with mounting ear

For applications when heavy loads up to 100kg

Material:

- SPCC Cold rolled steel t1.2

Surface Finish:

- Degreasing, pickling,

phosphoric, powder coat

Heavy-duty fixed shelf with mounting ear

## Dimension

Specification

| Model No. | Specification | Load (KG) | H | φ |
| --- | --- | --- | --- | --- |
| SESA.0026.001 | 2” heavy duty castor | 150 | 72 | 50.8 |
| SESA.0026.003 | 2” castor with brake | 150 | 72 | 50.8 |
| SESA.0026.004 | 2.5” heavy duty castor | 150 | 84.7 | 63.5 |
| SESA.0026.005 | 2.5” castor with brake | 150 | 84.7 | 63.5 |

# Heavy duty castor

# Surface Finish:

- Orchid Zinc

Castors

## Dimension

# Structure of sliding shelf

1. Guiding girder

2. 14” 2-section slide

3. Sliding loading plate

Sliding shelf

# Sliding shelf

# Material:

- SPCC cold rolled steel t1.2 /14”2-section slide

# Surface Finish:

- Degreasing, pickling, phosphoric, powder coated

# Parameter:

- Flexing length: 210MM   Loading capacity: 20KG

Specification                                                                Definition of color: SA.■■■■. ■■1:RAL9004       SA.■■■■. ■■2:RAL7035

| Model No. | Specification | Dimension(MM) | Use |
| --- | --- | --- | --- |
|  |  | W | D1 | D2 |  |
| SESA.6004.00■ | 60 Sliding shelf | 470 | 350 | 380 | 19” installation for 600-depth cabinets |
| SESA.8004.00■ | 80 Sliding shelf | 470 | 550 | 580 | 19” installation for 800-depth cabinets |
| SESA.9004.00■ | 90 Sliding shelf | 470 | 650 | 680 | 19” installation for 900-depth cabinets |
| SESA.9104.00■ | 100 Sliding shelf | 470 | 710 | 740 | 19” installation for 1000-depth cabinets |
| SESA.8604.00■ | 60 Extra-width Sliding shelf | 670 | 350 | 380 | 27” installation for 600-depth cabinets, remove cable management slot and spacer |
| SESA.8804.00■ | 80 Extra-width Sliding shelf | 670 | 550 | 580 | 27” installation for 800-depth cabinets, remove cable management slot and spacer |
| SESA.8904.00■ | 90 Extra-width Sliding shelf | 670 | 650 | 680 | 27” installation for 900-depth cabinets, remove cable management slot and spacer |
| SESA.8104.00■ | 100 Extra-width Sliding shelf | 670 | 710 | 740 | 27” installation for 1000-depth cabinets, remove cable management slot and spacer |

Аксесоари

Specification       Definition of color: SA.■■■■. ■■1:RAL9004

SA.■■■■. ■■2:RAL7035

| Model No. | Specification | Use |
| --- | --- | --- |
| SESA.0057.00■ | Adjustable Keyboard tray | 19” installation |

# Adjustable Keyboard panel

# Material:

- SPCC cold rolled steel t1.2 /14”2-section slide

# Surface Finish:

- Degreasing, pickling, phosphoric, powder coated

# Parameter:

- Flexing length: 210MM   Loading capacity: 20KG

Adjustable Keyboard panel

Dimension

Structure of Keyboard tray

# Adjustable Keyboard tray with small round lock

# Material:

- SPCC cold rolled steel t1.2 /14”2-section slide

# Surface Finish:

- Degreasing, pickling, phosphoric, powder coated

# Parameter:

- Flexing length: 210MM   Loading capacity: 20KG

Specification        Definition of color: SA.■■■■. ■■1:RAL9004

SA.■■■■. ■■2:RAL7035

| Model No. | Specification | Use |
| --- | --- | --- |
| SESA.0057.10■ | Adjustable Keyboard tray with small round lock | 19” installation |

Adjustable Keyboard panel with small round lock

Dimension

Аксесоари

## Dimension

Keyboard panel

# Keyboard panel

# Material:

- SPCC cold rolled steel t1.2 /14”2-section slide

# Surface Finish:

- Degreasing, pickling, phosphoric, powder coated

# Parameter:

- Flexing length: 210MM   Loading capacity: 20KG

1. Guiding girder

2. 14”2-section slide

3. Keyboard loading plate

Structure of Keyboard panel

Specification                                                             Definition of color: SA.■■■■. ■■1:RAL9004        SA.■■■■. ■■2:RAL7035

| Model No. | Specification | Dimension(MM) | Use |
| --- | --- | --- | --- |
|  |  | W | D1 | D2 |  |
| SESA.6005.00■ | 60 Keyboard tray | 470 | 350 | 380 | 19” installation for 600-depth cabinets |
| SESA.8005.00■ | 80 Keyboard tray | 470 | 350 | 580 | 19” installation for 800-depth cabinets |
| SESA.9005.00■ | 90 Keyboard tray | 470 | 350 | 680 | 19” installation for 900-depth cabinets |
| SESA.9105.00■ | 100 Keyboard tray | 470 | 350 | 740 | 19” installation for 1000-depth cabinets |
| SESA.8605.00■ | 60 Extra-width Keyboard tray | 670 | 350 | 380 | 27” installation for 600-depth cabinets, remove cable management slot and spacer |
| SESA.8805.00■ | 80 Extra-width Keyboard tray | 670 | 350 | 580 | 27” installation for 800-depth cabinets, remove cable management slot and spacer |
| SESA.8905.00■ | 90 Extra-width Keyboard tray | 670 | 350 | 680 | 27” installation for 900-depth cabinets, remove cable management slot and spacer |
| SESA.8105.00■ | 100 Extra-width Keyboard tray | 670 | 350 | 740 | 27” installation for 1000-depth cabinets, remove cable management slot and spacer |

Specification                                                               Definition of color: SA.1■■■. ■■■:RAL9004     SA.2■■■. ■■■:RAL7035

| Model No. | Specification | Dimension(MM) | N | Use |
| --- | --- | --- | --- | --- |
|  |  | L |  |  |
| SESA.■028.418 | 18U Cable management slot | 802.4 | 18 | A2/AS/AD 800-wdth cabinets and OR open Racks for 18U |
| SESA.■028.422 | 22U Cable management slot | 980.2 | 22 | A2/AS/AD 800-wdth cabinets and OR open Racks for 22U |
| SESA.■028.427 | 27U Cable management slot | 1202.5 | 27 | A2/AS/AD 800-wdth cabinets and OR open Racks for 27U |
| SESA.■028.432 | 32U Cable management slot | 1424.7 | 32 | A2/AS/AD 800-wdth cabinets and OR open Racks for 32U |
| SESA.■028.437 | 37U Cable management slot | 1647 | 37 | A2/AS/AD 800-wdth cabinets and OR open Racks for 37U |
| SESA.■028.442 | 42U Cable management slot | 1869.2 | 42 | A2/AS/AD 800-wdth cabinets and OR open Racks for 42U |
| SESA.■028.447 | 47U Cable management slot | 2091.5 | 47 | A2/AS/AD 800-wdth cabinets and OR open Racks for 47U |

# Cable management slot

Material:

- SPCC Cold rolled steel t1.2

Surface Finish:

- Degreasing, Pickling, Phosphoric, Powder coated

Color:

- RAL9004     RAL7035

## Dimension

Cable management slot

Аксесоари

Color

| RAL9004 | RAL7035 |
| --- | --- |
| black | gray |

Color:

- RAL9004

- RAL7035

### Dimension

### Dimension

Specification

| Model No. | Specification | Height(U) |
| --- | --- | --- |
| SESA.0020.01■ | 1U cable management with cap | 1U |
| SESA.0020.02■ | 2U cable management with cap | 2U |

1U, 2U Metal cable

management with cap

Metal cable management with cap

Material:

- SPCC Cold rolled steel t1.2

Surface Finish:

- Degreasing, Pickling, Phosphoric, Powder coat

Specification                                                             Definition of color: SA.■■■■. ■■2:RAL9004          SA.■■■■. ■■3:RAL7035

| Model No. | Specification | Dimension(MM) | Use |
| --- | --- | --- | --- |
|  |  | W | D | H | A1 | A2 |  |
| SESA.0040.11■ | 66 Plinth(100mm height) | 596 | 596 | 100 | 460 | 460 | 600-width and 600-depth A2/AS/AD cabinets |
| SESA.0040.21■ | 68 Plinth(100mm height) | 596 | 796 | 100 | 460 | 660 | 600-width and 800-depth A2/AS/AD cabinets |
| SESA.0040.31■ | 69 Plinth(100mm height) | 596 | 896 | 100 | 460 | 760 | 600-width and 900-depth A2/AS/AD cabinets |
| SESA.0040.41■ | 60 Plinth(100mm height) | 596 | 996 | 100 | 460 | 820 | 600-width and 1000-depth A2/AS/AD cabinets |
| SESA.0040.51■ | 86 Plinth(100mm height) | 796 | 596 | 100 | 660 | 460 | 800-width and 600-depth A2/AS/AD cabinets |
| SESA.0040.61■ | 88 Plinth(100mm height) | 796 | 796 | 100 | 660 | 660 | 800-width and 600-depth A2/AS/AD cabinets |
| SESA.0040.71■ | 89 Plinth(100mm height) | 796 | 896 | 100 | 660 | 760 | 800-width and 900-depth A2/AS/AD cabinets |
| SESA.0040.81■ | 80 Plinth(100mm height) | 796 | 996 | 100 | 660 | 820 | 800-width and 1000-depth A2/AS/AD cabinets |
| SESA.0040.12■ | 66 Plinth(200mm height) | 596 | 596 | 200 | 460 | 460 | 600-width and 600-depth A2/AS/AD cabinets |
| SESA.0040.22■ | 68 Plinth(200mm height) | 596 | 796 | 200 | 460 | 660 | 600-width and 800-depth A2/AS/AD cabinets |
| SESA.0040.32■ | 69 Plinth(200mm height) | 596 | 896 | 200 | 460 | 760 | 600-width and 900-depth A2/AS/AD cabinets |
| SESA.0040.42■ | 60 Plinth(200mm height) | 596 | 996 | 200 | 460 | 820 | 600-width and 1000-depth A2/AS/AD cabinets |
| SESA.0040.52■ | 86 Plinth(200mm height) | 796 | 596 | 200 | 660 | 460 | 800-width and 600-depth A2/AS/AD cabinets |
| SESA.0040.62■ | 88 Plinth(200mm height) | 796 | 796 | 200 | 660 | 660 | 800-width and 800-depth A2/AS/AD cabinets |
| SESA.0040.72■ | 89 Plinth(200mm height) | 796 | 896 | 200 | 660 | 760 | 800-width and 900-depth A2/AS/AD cabinets |
| SESA.0040.82■ | 80 Plinth(200mm height) | 796 | 996 | 200 | 660 | 820 | 800-width and 1000-depth A2/AS/AD cabinets |

A2/AS/AD plinth

### Dimension

## A2/AS/AD plinth

Material:

- SPCC cold rolled steel, Thickness: Plate 1.2MM,

others 2.0MM

Surface Finish:

- Degreasing, pickling, phosphoric, powder coated

Color:

- RAL9004       RAL7035

Аксесоари

Baying kits (for A2/AS/AD)

Specification

| Model No. | Specification |
| --- | --- |
| SESA.0033.001 | Baying kit (for A2/AS/AD cabinet) |

Connector (patent)

Connecting A2/AS cabinet without nuts, easy operation and safe

Material:

- SPCC cold rolled steel t2.0

Surface finish:

- Plated color Zinc

Remark: Move side doors when connect

Specification

| Model No. | Specification | Loading Capacity(KG) |
| --- | --- | --- |
| SESA.0025.011 | φ10 | 280 |

Adjustable Feet

Leveling legs allow cabinet to be leveled on the uneven surface

Material:

- Steel

Surface finish:

- Carbonic white

Adjustable Feet

Keyboard with mouse panel

Small round lock

Specification

| Model No. | Spring height（MM） |
| --- | --- |
| SESA.0027.001 | 103-25,universal key |
| SESA.0027.004 | 103-20,universal key |
| SESA.0027.005 | 103-16,universal key |
| SESA.0027.006 | 103-16, side panel lock (with sheet metal) |

#### Small round lock

■    Simple structure, economic, operate easily

Surface finish:

■    Plated Nickel

Cooling fan

Specification

| Model No. | Specification | Voltage |
| --- | --- | --- |
| SESA.0014.001 | Cooling fan | 220V |
| SESA.0014.002 | Cooling fan | 110V |
| SESA.0014.003 | Cooling fan(Direct current) | 48V |
| SESA.0014.004 | Cooling fan(ball bearing ) | 220V |
| SESA.0014.005 | Cooling fan(ball bearing ) | 110V |
| SESA.0014.006 | Cooling fan(Direct current/ball bearing) | 48V |

##### Cooling fan

Lower-noise, long lifespan, plastic filter optional

Dimension:

- 120mm*120mm*38mm

Mounting dimension:

- 105mm*105mm

Air flowing:

- 50-110CBM/H

Specification

| Model No. | Specification | Height (U) |
| --- | --- | --- |
| SESA.0022.00■ | Keyboard with mouse panel | 2U |

#### Keyboard with mouse panel

19” cabinet, keyboard with mouse, easy to operate

Material:

- SPCC cold rolled steel t1.2/12” 3pcs sliding rails

Surface finish:

- Degreasing, pickling, phosphoric, powder coated

Parameter:

- Flexing length: 220mm   loading capacity: 20 KG

3” Heavy duty Castor with brake

Surface finish:

- Orchid Zinc

Castor with two wheels

Surface finish:

- Orchid Zinc

Specification

| Model No. | Specification | Load (KG) |
| --- | --- | --- |
| SESA.0026.007 | 3” heavy duty Castor with brake | 150 |

Specification

| Model No. | Specification | Load (KG) |
| --- | --- | --- |
| SESA.0026.006 | 2” heavy duty Castor with two wheel | 240 |

3” heavy duty Castor with brake

Castor with two wheel

Аксесоари

Spring lock

Advanced moon-shaped lock

#### Spring lock

Spring lock with spinning structure, handle will be automatically open front, surface with special coating

Surface finish:

- Black oxidation powdered

Specification

| Model No. | Specification |
| --- | --- |
| SESA.0027.003 | Advanced moon-shaped lock |

Advance moon-shaped lock

Surface in silver gray, spinning structure, special surface with coating

Surface finish:

- Oxidation powdered

Аксесоари

Specification:

| Model No. | Specification |
| --- | --- |
| SESA.0027.002 | Spring lock (without lock pin) |
| SESA.0027.007 | Spring lock (for AD cabinet) |
| SESA.0027.008 | Spring lock (for AS cabinet) |

Definition of color:

SA.■■■■. ■■1:RAL9004

SA.■■■■. ■■2:RAL7035

Blanking panel

Specification

| Model No. | Specification | Height (U) |
| --- | --- | --- |
| SESA.0006.01■ | 1U Blanking panel | 1U |
| SESA.0006.02■ | 2U Blanking panel | 2U |
| SESA.0006.04■ | 4U Blanking panel | 4U |

# Blanking panel

■    19” cabinets as blanking plate

Material:

■    SPCC cold rolled steel t1.2

Surface Finish:

■    Degreasing, pickling, phosphoric, powder coated

Color:   RAL9004      RAL7035

Definition of color:

SA.■■■■. ■■1:RAL9004

SA.■■■■. ■■2:RAL7035

Specification

| Model No. | Specification | Height(U) |
| --- | --- | --- |
| SESA.0020.03■ | 1U Plastic cable management | 1U |

# 1U Plastic cable management

19” cabinet, removable plastic cable management ring

Material:

■    SPCC t1.5/plastic cable management ring

Surface Finish:

■    Degreasing, pickling, phosphoric, powder coated

Color:   RAL9004      RAL7035

1U Plastic cable management

Definition of color:

SA.■■■■. ■■1:RAL9004

SA.■■■■. ■■2:RAL7035

Specification

| Model No. | Specification | Height(U) |
| --- | --- | --- |
| SESA.0020.04■ | 1U Metal cable management | 1U |

1U Metal cable management

# 1U Metal cable management

19” cabinet, removable metal cable management ring

Material:

■    SPCC t1.5/metal cable management ring

Surface Finish:

■    Degreasing, pickling, phosphoric, powder coated

Color:   RAL9004     RAL7035

Display panel

Аксесоари

Definition of color:

SA.■■■■. ■■1:RAL9004

SA.■■■■. ■■2:RAL7035

Definition of color:

SA.■■■■. ■■1:RAL9004

SA.■■■■. ■■2:RAL7035

Specification

| Model No. | Specification | Height(U) |
| --- | --- | --- |
| SESA.0043.19■ | 1U Plastic cable management | 1U |

# Shunting rail

■    Use for 19” cabinets fastening cables

Material:

■    SPCC cold rolled steel t1.5

Surface Finish:

■    Degreasing, pickling, phosphoric, powder coated

Color:   RAL9004       RAL7035

Shunting rail

Specification

| Model No. | Specification | Dimension of Window |
| --- | --- | --- |
| SESA.0012.15■ | 15” display panel | 285*215 |
| SESA.0012.17■ | 17” display panel | 320*240 |

# Display Panel

■    19” cabinets as display plate with height 10U

Material:

■    SPCC cold rolled steel t1.2

Surface Finish:

■    Degreasing, pickling, phosphoric, powder coated

Color:   RAL9004     RAL7035

Specification

| Model No. | Color |
| --- | --- |
| SESA.0031.002 | White |
| SESA.0031.003 | Black |

Plastic cable management ring

For cables in network cabinets

Material:

- Plastic

Height:

- 2U

Plastic cable management ring

Plastic cable management slot

Specification

| Model No. | Specification | Length (M) |
| --- | --- | --- |
| SESA.0028. 200 | 35*35 | 2±0.02 |
| SESA.0028. 201 | 50*50 | 2±0.02 |
| SESA.0028. 2■■ | 35*35 | Based on U mark |
| SESA.0028. 3■■ | 50*50 | Based on U mark |

Plastic cable management slot

Use for cables in cabinets

Color:

- Close to RAL6034

Definition of color:

SA.■■■■. ■■1: RAL9004

SA.■■■■. ■■2: RAL7035

Specification

| Model No. | Spec. | Use |
| --- | --- | --- |
| SESA.6001.00■ | 60L rail | 600-depth cabinets |
| SESA.8001.00■ | 80L rail | 800-depth cabinets |
| SESA.9001.00■ | 90L rail | 900-depth cabinets |
| SESA.9101.00■ | 96L rail | 960-depth cabinets |

# L rail

Fastened to mounting rails for supporting equipment

Material:

- SPCC cold rolled steel t1.5

Surface Finish:

- Degreasing,Pickling,Phosphoric,Powder coated

Color:  RAL9004       RAL7035

L rail

Screws & nuts with cushion

Specification

| Model No. | /bag |
| --- | --- |
| SESA.0021.003 | 20pcs |

Screws and nuts with cushion

Specification:

- Screw：M6*16 ;Nut：M6

Washer:Φ6

Surface finish:

- Plated Nickel

Аксесоари

Metal cable management ring

Specification

| Model No. | Height(U) |
| --- | --- |
| SESA.0031.011 | For left hand of A2/AS cabinet |
| SESA.0031.012 | For right hand of A2/AS/AD cabinet |

# Metal cable management ring

For cables in network cabinets

Material:

- SPCC cold rolled steel

Color:

- RAL9004

- RAL7035

- Plated Nickel

Аксесоари

Advanced screws & nuts

Specification

| Model No. | /bag |
| --- | --- |
| SESA.0021.002 | 20pcs |

## Advanced screws & nuts

Specification:

- Screw：M6*12 ;nut：M6

#### Surface finish:

- Plated Nickel

1U fan unit

# 1U fan unit

For network cabinet, adjust inner temperature

Parameter:

■  period: 0~50℃, input: 220VAC/115VAC

Material:

■  SPCC cold rolled steel t1.2

Surface finish:

■  Degreasing, pickling, phosphoric, powder coated

Color:  RAL9004      RAL7035

Specification

| Model No. | Specification | Remark |
| --- | --- | --- |
| SESA.0018.2■■ | 1U fan unit with 2fans | 2 fans |
| SESA.0018.3■■ | 1U fan unit with 3fans | 3 fans |
| SESA.0018.4■■ | 1U fan unit with 4fans | 4 fans |

Inner 6-angle screws & nuts

Specification

| Model No. | /bag |
| --- | --- |
| SESA.0021.001 | 20pcs |

### Inner 6-angle screws & nuts

Specification:

- Screw：M6*12 ;nut：M6

Surface finish:

- Plated color Zinc

1U fan unit with thermostat

Color

| RAL9004 | RAL7035 |
| --- | --- |

Definition of last 2 number for color

| Model Number | Color Number |
| --- | --- |
| SA.■■■■.■1■ | RAL9004 |
| SA.■■■■.■2■ | RAL7035 |

Definition of last number for type of plug

| Model Number | Type of plug | Voltage/HZ | Current |
| --- | --- | --- | --- |
| SA.■■■■.■■0 | All-usage type | 220V/50-60Hz | 10A |
| SA.■■■■.■■1 | US type | 110V/50-60Hz | 10A |
| SA.■■■■.■■2 | German type | 220V/50-60Hz | 16A |
| SA.■■■■.■■3 | UK type | 220V/50-60Hz | 13A |

Specification

# 1U fan unit with the thermostat

For network cabinet, adjust inner temperature

Parameter:

■  period: 0~50℃, input: 220VAC/115VAC

Material:

■  SPCC cold rolled steel t1.2

Surface finish:

■  Degreasing, pickling, phosphoric, powder coated

Color:  RAL9004      RAL7035

Аксесоари

| Model No. | Specification | Remark |
| --- | --- | --- |
| SESA.0038.2■■ | 1U fan unit with 2fans and thermostat | 2 fans |
| SESA.0038.3■■ | 1U fan unit with 3fans and thermostat | 3 fans |
| SESA.0038.4■■ | 1U fan unit with 4fans and thermostat | 4 fans |

Color

| RAL9004 | RAL7035 |
| --- | --- |
| black | gray |

Specification of cable plug

| Model No. | Specification | V | A | Remark |
| --- | --- | --- | --- | --- |
| SA.■■■■.■■1 | UL-type | 110V | 10A | Overseas market |
| SA.■■■■.■■2 | German-type | 220V | 16A | Overseas market |
| SA.■■■■.■■3 | UK-type | 220V | 13A | Overseas market |
| SA.■■■■.■■4 | All-usage | 220V | 10A | Overseas market |

Definition of color

| Model No. | color |
| --- | --- |
| SA.■■■■.■1■ | RAL9004 |
| SA.■■■■.■2■ | RAL7035 |

A2/AS/AD Fan unit

Material:

- SPCC cold rolled steel

Thickness:

- Power cord box:1.2mm;

- Fan tray:0.8mm

Surface Finish:

- Degreasing,pickling,phosphoric,powder coated

Color:

- RAL9004      RAL7035

Specification

| Model No. | Specification | Dimension (MM) | Use |
| --- | --- | --- | --- |
|  |  | W | D | A | B |  |
| SESA.0015.6■■ | Fan unit for 600mm DP A2/AS/AD cabinet: 2fans | 450 | 351 | 360 | 331 | A2/AS/AD 600mm DP cabinet: 2 cooling fans |
| SESA.0015.8■■ | Fan unit for 800mm DP A2/AS/AD cabinet: 4fans | 450 | 551 | 360 | 531 | A2/AS/AD 800mm DP cabinet: 4 cooling fans |
| SESA.0015.9■■ | Fan unit for 900mm DP A2/AS/AD cabinet: 4fans | 450 | 651 | 360 | 631 | A2/AS/AD 900mm DP cabinet: 4 cooling fans |
| SESA.0015.1■■ | Fan unit for 1000mm DP A2/AS/AD cabinet: 4fans | 450 | 751 | 360 | 731 | A2/AS/AD 1000mm DP cabinet: 4 cooling fans |

A2/AS/AD Fan unit

Dimension

Аксесоари

Specification

| Model No. | Specification | Dimension-Depth(MM) | H(MM) | Thickness (MM) | Remark |
| --- | --- | --- | --- | --- | --- |
| SESA.0052.00■ | 1U,10” – DP cantilever shelf - III | 266.7 | 31.8 | 1.5 | 19” installation |
| SESA.0052.01■ | 1U,15” – DP cantilever shelf - III | 381 | 31.8 | 1.5 | 19” installation |
| SESA.0052.02■ | 2U,10” – DP cantilever shelf - III | 266.7 | 76.2 | 1.5 | 19” installation |
| SESA.0052.03■ | 2U,15” – DP cantilever shelf - III | 381 | 76.2 | 1.5 | 19” installation |

Dimension

Specification

| Model No. | Specification | Dimension-Depth(MM) | Thickness (MM) | Remark |
| --- | --- | --- | --- | --- |
| SESA.0009.45■ | 45 Cantilever shelf - I | 300 | 1.5 | 19” installation |
| SESA.0009.60■ | 60 Cantilever shelf - I | 350 | 1.5 | 19” installation |
| SESA.0009.80■ | 80 Cantilever shelf - I | 550 | 1.5 | 19” installation |
| SESA.0009.96■ | 100 Cantilever shelf - I | 710 | 1.5 | 19” installation |

Cantilever shelf - II

Cantilever shelf - II

Material:

- SPCC cold rolled steel

Surface Finish:

- Degreasing,picking,phosporic,

powder coated

Standard color:

- RAL9004

- RAL7035

Cantilever shelf - III

Dimension

Cantilever shelf - III

Material:

- SPCC cold rolled steel

Surface Finish:

- Degreasing,picking,phosporic,

powder coated

Standard color:

- RAL9004

- RAL7035

Color

| RAL9004 | RAL7035 |
| --- | --- |
| black | gray |

Definition of color

| Model No. | Color |
| --- | --- |
| SA.■■■■.■■1 | RAL9004 |
| SA.■■■■.■■2 | RAL7035 |

Specification

| Model No. | Specification | Dimension-Depth(MM) | H(MM) | Thickness (MM) | Remark |
| --- | --- | --- | --- | --- | --- |
| SESA.0051.00■ | 1U,10” – DP cantilever shelf - II | 266.7 | 31.8 | 1.5 | 19” installation |
| SESA.0051.01■ | 1U,15” – DP cantilever shelf - II | 381 | 31.8 | 1.5 | 19” installation |
| SESA.0051.02■ | 2U,10” – DP cantilever shelf - II | 266.7 | 76.2 | 1.5 | 19” installation |
| SESA.0051.03■ | 2U,15” – DP cantilever shelf - II | 381 | 76.2 | 1.5 | 19” installation |

Cantilever shelf - I

Dimension

Cantilever shelf - I

Material:

- SPCC cold rolled steel

Surface Finish:

- Degreasing,picking,phosporic,powder coated

Standard color:

- RAL9004

- RAL7035

Specification

| Model No. | Specification | Dimension-Depth(MM) | Thickness (MM) | Remark |
| --- | --- | --- | --- | --- |
| SESA.0056.45■ | 2U, 45 Cantilever shelf with mounting ear | 300 | 1.5 | 19” installation |
| SESA.0056.60■ | 2U, 60 Cantilever shelf with mounting ear | 350 | 1.5 | 19” installation |
| SESA.0056.80■ | 2U, 80 Cantilever shelf with mounting ear | 550 | 1.5 | 19” installation |
| SESA.0056.90■ | 2U, 90 Cantilever shelf with mounting ear | 650 | 1.5 | 19” installation |
| SESA.0056.96■ | 2U, 100 Cantilever shelf with mounting ear | 710 | 1.5 | 19” installation |

Specification

| Model No. | Specification | H(MM) | Thickness (MM) | Remark |
| --- | --- | --- | --- | --- |
| SESA.0019.02■ | 2U Height Drawer | 88 | 1.5 & 1.2 | 19” installation |
| SESA.0019.03■ | 3U Height Drawer | 132 | 1.5 & 1.2 | 19” installation |
| SESA.0019.04■ | 4U Height Drawer | 178 | 1.5 & 1.2 | 19” installation |
| SESA.0019.05■ | 5U Height Drawer | 222 | 1.5 & 1.2 | 19” installation |

Dimension

Specification

| Model No. | Specification | Dimension-Depth(MM) | Thickness (MM) | Remark |
| --- | --- | --- | --- | --- |
| SESA.0055.45■ | 1U, 45 Cantilever shelf with mounting ear | 300 | 1.5 & 2.0 | 19” installation |
| SESA.0055.60■ | 1U, 60 Cantilever shelf with mounting ear | 350 | 1.5 & 2.0 | 19” installation |
| SESA.0055.80■ | 1U, 80 Cantilever shelf with mounting ear | 550 | 1.5 & 2.0 | 19” installation |
| SESA.0055.90■ | 1U, 90 Cantilever shelf with mounting ear | 650 | 1.5 & 2.0 | 19” installation |
| SESA.0055.96■ | 1U, 100 Cantilever shelf with mounting ear | 710 | 1.5 & 2.0 | 19” installation |

2U Height Cantilever shelf with mounting ear

2U Height Cantilever shelf with mounting ear

Material:

- SPCC cold rolled steel

Surface Finish:

- Degreasing,picking,phosporic,

powder coated

Standard color:

- RAL9004      RAL7035

Drawer

Dimension

Drawer

Material:

- SPCC cold rolled steel/14”2-section slide

Surface Finish:

- Degreasing,picking,phosporic,

powder coated

Standard color:

- RAL9004      RAL7035

Color

| RAL9004 | RAL7035 |
| --- | --- |
| black | gray |

Definition of color

| Model No. | Color |
| --- | --- |
| SA.■■■■.■■1 | RAL9004 |
| SA.■■■■.■■2 | RAL7035 |

1U Height Cantilever shelf with mounting ear

Dimension

1U Height Cantilever shelf with mounting ear

Material:

- SPCC cold rolled steel

Surface Finish:

- Degreasing,picking,phosporic,powder coated

Standard color:

- RAL9004       RAL7035

Аксесоари

Specification

| Model No. | Specification | Dimension (MM) | Thickness(MM) | Use |
| --- | --- | --- | --- | --- |
|  |  | H | D |  |  |
| SESA.0048.04■ | 4U Wall mount bracket | 180 | 304.8 | 1.5 | 19” installation |
| SESA.0048.06■ | 6U Wall mount bracket | 269 | 304.8 | 1.5 | 19” installation |

Specification

| Model No. | Specification |
| --- | --- |
| SA.0023.000 | 16W,with 2m power cord & 2 flat pins |

Energy saving tube

Energy saving tube

With CE & CCC certification

Specification

| Model No. | Specification | Use |
| --- | --- | --- |
| SA.0050.00■ | Cable entry with brush | With 2 brush |

Cable entry with brush

Cable entry with brush

Material:

- SPCC cold rolled steel,

Thickness: 1.2MM

Surface finish:

- Degreasing,picking,phosphoric,

powder coated

Standard color:

- RAL9004     RAL7035

Color

| RAL9004 | RAL7035 |
| --- | --- |
| black | gray |

Definition of Color

| Model No. | Color |
| --- | --- |
| SA.■■■■.■■1 | RAL9004 |
| SA.■■■■.■■2 | RAL7035 |

Specification

| Model No. | Specification | Use |
| --- | --- | --- |
| SA.0049.00■ | 1U Brush type cable | With 1 brush |

1U Brush type cable management

Wall mount bracket

Dimension

1U Brush type cable

management

Material :

- SPCC cold rolled steel,

Thickness: 1.2MM

Surface finish:

- Degreasing,picking,phosphoric

powder coated

Standard color:

- RAL9004    RAL7035

Wall mount bracket

Material:

- Spcc cold rolled steel,

Thickness: 1.5mm

Surface finish:

- Degreasing,pickling,phosphoric,powder coated

Standard color:

- RAL9004       RAL7035